## Slide 1: Energy Networks Association
ENA EREC C81 Issue 6 2021
Revision Summary
13 July 2021

## Slide 2: ENA EREC C81 Issue 6 2021 Revision Summary
Type Approval Tests for Accessories for 600/1000 Volt Cable Systems
Details the performance and type testing requirements of cable accessories for use with power distribution cables of rated voltage 0,6/1,0 (1,2) kV as defined in BS EN 50393, BS EN 61238, BS 7870 and other relevant cable standards
  SCOPE
  Cable accessories including joints, stop ends, outdoor terminations for extruded solid dielectric insulated cables and transition joints between extruded solid dielectric insulated and impregnated paper insulated cables, but not specifically underground cable to overhead line transition joints
  HISTORY
  1st issued: Unknown
  1999: Minor revision of Issue 3 to reflect changes in BS Standards and ensure compliance with the Utilities Supply and Works Regulations 1992
  2021: Major revision as detailed overleaf
PURPOSE

## Slide 3: ENA EREC C81 Issue 6 2021 Revision Summary
Summary of Amendments
  Joints, stop ends and outdoor terminations for impregnated paper insulated cables are no longer included
  List of normative references updated
  List of definitions added
  Clause 4, Components: Direct reference to BS EN 50393 added
  Clause 5, Electrical Characteristics: Direct reference to BS EN 50393 added
  Clause 6, Range of Compliance: Direct reference to BS EN 50393 added
  Clause 7, Type Tests: Direct reference to BS EN 50393 added
  Clause 8, Test Methods: Direct reference to BS EN 50393 added
  Clause 8.1, Cantilever Load Withstand Test: Additional requirement for a Cantilever Load Withstand Test added
Major changes to requirements
Defers to BS EN 50393 for type approval tests of accessories for 600/1000v cable systems
Additional requirement for a Cantilever Load Withstand Test
Major
Key Points
Nature of Revision

## Slide 4: ENA EREC C81 Issue 6 2021 Revision Summary
Who is affected and why?
  Staff, who are tasked with the specification and procurement of cable accessories for use with power distribution cables of rated voltage 0,6/1,0 (1,2) kV
  ENA Member Companies should review their relevant technical specification(s) in relation to the amended requirements and update as necessary

## Slide 5: ENA EREC C81 Issue 6 2021 Revision Summary
 | Rating | Assessment
Safety | Nil | 
Environment | Nil | 
Financial (costs/benefits) | Minor | Additional requirement for Cantilever Load Withstand Test may increase price
Asset Quality & Performance | Minor | Potential for small reduction in premature joint failures following installation
Statutory/ Regulatory | Nil | Statutory requirements unchanged
Reputation | Nil | 
Impact Assessment

## Slide 6: ENA EREC C81 Issue 6 2021 Revision Summary
Summary and Actions
  ENA EREC C81 Issue 5 2021 is a major revision of Issue 4
  ENA Member Companies review their relevant technical documentation for cable accessories for use with power distribution cables of rated voltage 0,6/1,0 (1,2) kV
    The document is available from the ENA Engineering Catalogue at www.energynetworks.org.

## Slide 7
© ENA 2021