## Slide 1: Energy Networks Association
EREC G105 Issue 2 2026
Revision Summary
7th of July 2026

## Slide 2: EREC G105 Issue 2 2026 Revision Summary
Management of Reyrolle U-shaped ‘“hairpin’” nitrogen sealed current transformers
Establishes a management philosophy for the UK installed population of Reyrolle U-shaped hairpin nitrogen sealed CTs which are considered to be at risk of experiencing disruptive failure based on operational history.
A summary of failures of Reyrolle “hairpin’ CTs is discussed, alongside the associated failure modes.
The use of restricted access zones is explained and suggested thresholds for oil moisture and DGA levels are presented.
  SCOPE
    This EREC intends to provide recommendation for the management of the CTs to promote a consistent approach across differing ENA Member Companies (ENA MCs) until the suitability for continued service of the CTs is assessed, or a replacement programme is implemented.
  HISTORY
    1st Issue: 2018
    2nd Issue: May 2026 – Minor revision
DOCUMENT PURPOSE
2

## Slide 3
Summary of Amendments
    Update to international and national references
    Introduction – List of DINs and SOPs updated to reflect those issued since this EREC was last issued
    Table 2 - Updated with latest populations of Reyrolle “hairpin” CTs” in individual ENA MCs
    Tables 3 to 6 - Reproduced to assist with comparison of gas threshold levels between different normative references
    Annex A.2.4.2 - Added to cover exposure to members of the public
      Restricted access zone of one or multiple Reyrolle “hairpin” CTs may extend beyond the perimeter of the substation site into areas where members of the public may be present
      Risk assessment considers typical activities of members of the public and frequency of these activities which may be carried out close to affected substation
    Update to latest populations of affected CTs in ENA MCs
    Risk assessment methodology added in Issue 2 to assess risk to members of the public in cases where the restricted access zone extends outside substation into areas where members of public may be present
Minor
Key Points
Nature of Revision
3
EREC G105 Issue 2 2026 Revision Summary

## Slide 4: EREC G105 Issue 2 2026 Revision Summary
Who is affected and why?
    Risk of disruptive failure of CTs leading to risk to safety of staff who may enter substations where Reyrolle U-shaped ‘“hairpin’” CTs are in service
    Risk to members of the public in cases where restricted access zone of CTs requiring intervention extends beyond the perimeter of the substation site
    Recommendations on maximum concentrations of hydrogen and hydrocarbons and moisture levels of affected CTs before intervention is needed
    EREC G105 provides guidance on implementation of restricted access zones around CTs and maximum staff exposure limits where CT tests exceed recommended levels
    A minor revision was completed.
    The additional guidance should be useful to staff of ENA MCs with populations or Reyrolle hairpin CTs
4

## Slide 5
Impact Assessment
5
EREC G105 Issue 2 2026 Revision Summary
 | Rating | Assessment
Safety | Major | Risk to staff or public in event of disruptive failure of Reyrolle “hairpin” CT unit leading to dispersal of debris over large distance from CT
Environment | Low | No significant impact on environment
Financial (costs/benefits) | Medium | Additional costs in testing and or replacement of CTs
Asset Quality & Performance | Medium | Frequent testing of Reyrolle “hairpin” CT in accordance with EREC G105 is recommended to avoid failures in service and impact on network performance
Statutory/ Regulatory | Low | Management of Reyrolle hairpin CTs in accordance with EREC G105 may be necessary for Regulatory compliance of industry best practice for condition of assets
Reputation | Medium | Catastrophic failure leading to risks to staff or public can impact reputation

## Slide 6
Summary and Actions
    EREC G105 Issue 2 2026 is a minor revision of Issue 2
    ENA MCs should review and update as required their maintenance procedures for Reyrolle “hairpin” CTs to check oil moisture and oil DGA levels are below recommended thresholds.
    ENA MCs should review risk assessment procedures for management of Reyrolle hairpin CTs as required including possible implementation of restricted access zones where oil testing or other tests demonstrate values outside recommended thresholds.
    The document is available from the ENA Engineering Catalogue at www.energynetworks.org.
6
EREC G105 Issue 2 2026 Revision Summary

## Slide 7
© ENA 2026
7