## Slide 1: Energy Networks Association
ENA EREC C79 Issue 4 2021
Revision Summary
06 October 2021

## Slide 2: ENA EREC C79 Issue 4 2021 Revision Summary
Type tests for connectors for copper and aluminium conductors of insulated power cables with a rated voltage up to 36kV (Um 42kV)
Details the performance requirements of compression or mechanical connectors, including IPCs, for power cables with Water Blocked and Non-Water Blocked versions of copper or aluminium conductors.
  SCOPE
    Terminal connectors (lugs), Through (straight) connectors and Branch connectors.
    Is not applicable to connectors for overhead conductors, which are designed for special mechanical requirements, or separable connectors with sliding contacts or multi-core connectors, e.g. ring connectors.
    Conductor cross-sections covered are as follows; Copper: 2.5 - 1200 mm2. Aluminium: 16 - 1200 mm2.
  HISTORY
    1st issued: not known
    2009: Issue 2 published
    2014: Minor revision of Issue 2 with no principal technical changes
    2021: Major revision as detailed overleaf
DOCUMENT PURPOSE
2

## Slide 3: ENA EREC C79 Issue 4 2021 Revision Summary
Summary of Amendments
    Foreword: Information added to reflect the current text of BS EN IEC 61238-1, introduce new variants of BS EN IEC 61238-1 and update references to The Utilities Contract Regulations 2016 and EREC G79 Part 1 Issue 3:2019.
    Clause 1: Cross sectional area of conductors covered in this EREC amended to reflect BS EN IEC 61238-1.
    Reference to Water Blocked and Non-Water Blocked versions of conductors included.
    Note added referring to additional testing of Water Blocked versions being subject to agreement between Purchaser and Manufacturer/Supplier.
    Clause 3: Updated to align with BS EN IEC 61238-1.
    Clauses 4-7 inclusive: Updated to make direct reference to relevant clauses in appropriate variant of BS EN IEC 61238-1.
    Table 1: Load current pick-up values for stranded and solid aluminium conductors deleted Annex A (normative): Information required for notice of conformity deleted
    Annex B (normative): Example of the form of a notice of conformity deleted
    Bibliography added
Major changes to requirements
Defers to BS EN IEC 61238-1-1; -2;-3. for Type Approval Tests of connectors for copper and aluminium conductors of insulated power cables with a rated voltage up to 36kV (Um 42kV)
Specific reference to Water Blocked and Non Water Blocked conductors included
Major
Key Points
Nature of Revision
3

## Slide 4: ENA EREC C79 Issue 4 2021 Revision Summary
Who is affected and why?
    Primarily, staff, who are tasked with the procurement, approval and use of connectors for copper and aluminium conductors of insulated power cables with a rated voltage up to 36kV (Um 42kV)
    ENA Member Companies should review their relevant documentation and update as necessary
4
    As a major revision, the additional guidance should be useful for staff of ENA Member Companies

## Slide 5: ENA EREC C79 Issue 4 2021 Revision Summary
Impact Assessment
5
 | Rating | Assessment
Safety | Nil | 
Environment | Nil | 
Financial (costs/benefits) | Minor | Minimal impact anticipated
Asset Quality & Performance | Minor | Potential for minor performance improvement
Statutory/ Regulatory | Nil | Statutory requirements unchanged
Reputation | Nil | 

## Slide 6: ENA EREC C79 Issue 4 2021 Revision Summary
Summary and Actions
    ENA EREC C79 Issue 4 2021 is a major revision of Issue 3
    ENA Member Companies to review their relevant documentation and operating procedures for the procurement, approval and use of connectors for copper and aluminium conductors of insulated power cables with a rated voltage up to 36kV (Um 42kV)
6
    The document is available from the ENA Engineering Catalogue at www.energynetworks.org.

## Slide 7
© ENA 2020
7