## Slide 1: Energy Networks Association
ENA TS 43-8 Issue 6 2026
Revision Summary
26th January 2026

## Slide 2: ENA TS 43-8 Issue 6 2026 Revision Summary
Overhead line clearances
Defines the minimum clearance for ENAMC overhead lines.
  SCOPE
    This ENA TS defines the minimum clearance between ENAMC overhead lines at all all nominal system voltages and objects, ground, railway property and other ENAMC overhead lines.
  HISTORY
    1st Issue: Not known
    2nd Issue: 1988
    3rd Issue: 2004
    4th Issue: 2015
    4th Issue+A1: 2016
    5th Issue: June 2019
    6th Issue: February 2026 – Medium revision
DOCUMENT PURPOSE
2

## Slide 3: ENA TS 43-8 Issue 6 2026 Revision Summary
Summary of Amendments
    Update to references.
    Clause 6.2 – Reference to EREC L44. Also, note of lack of existing industry standards for clearance to BESS and solar farms hence only guidance is to apply site-specific risk assessments.
    Clause 6.3.4 – Addition of bullet point c) to state that where clearances in Table 3 cannot be achieved then the ENAMC shall risk assess the clearance.
    Clause 11.1 – Clarity on work activities near OHLs and application of term ‘ordinarily accessible’ to distinctly separate Table 2 and Clause 11.
    Update to references.
    Greater clarity in Clause 6.3.4 and Clause 11 for where clearances can/cannot be maintained, to follow a risk assessment approach.
Medium
Key Points
Nature of Revision
3

## Slide 4: ENA TS 43-8 Issue 6 2026 Revision Summary
Who is affected and why?
    Primarily, staff who are tasked with overhead line design and ensuring that sufficient clearances are maintained for ENAMC overhead lines. ENA Member Companies should review their relevant documentation and update, as necessary.
    A medium revision was completed, the additional guidance should be useful for staff of ENA Member Companies
4

## Slide 5: ENA TS 43-8 Issue 6 2026 Revision Summary
 | Rating | Assessment
Safety | 2 | Some minor amendments to the risk assessment criteria for DNOs assessing LV systems attached to buildings.
Environment | Nil | 
Financial (costs/benefits) | Nil | 
Asset Quality & Performance | Nil | 
Statutory/ Regulatory | 1 | Inclusion of ESQCR Reg 18 wording to dictate risk of using bare wire conductors with phase conductor above neutral.
Reputation | Nil | 
Impact Assessment
5

## Slide 6: ENA TS 43-8 Issue 6 2026 Revision Summary
Summary and Actions
    ENA TS 43-8 Issue 6 2026 is a medium revision of Issue 5.
    ENA Member Companies to review and update their overhead line clearances documents.
    The document is available from the ENA Engineering Catalogue at www.energynetworks.org.
6

## Slide 7
© ENA 2026
7